## Slide 1: Computer Network Assignments

## Slide 2: #1. Chapter 1-8
1. List the layers in the TCP/IP model, and give a brief explanation of each.
2. Is it possible to develop Internet applications without understanding the architecture of the Internet and the technologies? Support your answers.
3. Compare and contrast a client and server application by summarizing characteristics of each.
4. If a sender wants to have copies of each data block being sent to ten recipients, which (transport) paradigm should the sender choose?
5. How CRC and checksum are produced in real communication?
Why is CRC at the tail of a packet? Why is checksum in the header of a packet?
6. What can a RAC scheme achieve that a single parity bit scheme cannot?
7. For a channel with a 1 MHz bandwidth and S/N ratio of 63, what are the effective limit on channel capacity (in bps) and the number of signal levels?
8. If the length of antenna is a half of the signal’s wavelength, determine the length of antenna to receive an electromagnetic signal with f=10GHz and propagation speed of 1.5X108 m/sec.
9. Show the rate at which three digital voice data are sent at the same time using PCM in a digital telephone system.
10. Find out the MAC address and IP address of your computer using “ipconfig”.
11. Find out the path(router addresses) from your computer to “www.dankook.ac.kr” using “tracert”.
12. Find some information about “wireshark”, and install it on your computer.
13. List typical wired transmission media with the type of its signal.
14. What two identifiers are used to specify a particular server?

## Slide 3: #2. Chapter 9-16
1. We need to use synchronous TDM and combine 10 digital sources, each of 800bps. Each output slot carries 8 bits from each source,
but one extra bit(framing bit) is added to each frame.
a) what is the size of an output frame in bits?
b) What is the output data rate(bps)?
2. In case of sending data “1111010” through RS-232C, illustrate the bit flows including start, parity, and stop bit.
3. What is the difference between shift keying and modulation?
4. Consider a link of 1000m with a bandwidth of 1Gbps, and the propagation speed of 108 m/sec.
a) What is the propagation delay through this line?
b) What is the transmission delay of a packet of 1000bytes?
c) How many bits can be contained in the link at most?
5. Compare the throughput of the following transmissions.
a) parallel vs. serial b) FDM vs. TDM
c) full-duplex vs. half-duplex d) synchronous vs. asynchronous
6. An Ethernet MAC sublayer receives 24bytes of data from the upper layer. What is the size of an Ethernet frame containing the data?
7. What are the fields in a Ethernet frame? Explain each field(size and content).
8. If someone wanted to broadcast a copy of a video presentation, is a circuit switching system or a packet switching preferable? Why?
9. a) In the CSMA protocol, what happens if two stations wait for the cable to be idle?
b) How is this problem handled in CSMA/CD?
10. Why is there no need for CSMA/CD on a full-duplex Ethernet LAN?
11. Compare Ethernet hubs and Layer2 switches.
12. Capture Ethernet frames using “Wireshark” and find out how your computer’s MAC address(found through command “ipconfig”) is used.

## Slide 4: Mid-Term Exam. Schedule
Date:
Div.1 : 4. 19(Thur.) 14:15 – 15:30
Div.5 : 4. 19(Thur.) 15:30 – 17:00
Coverage
- Chapter 1. – Chapter. 18.
No Classes on 4.23(Mon.)/ 4.24(Tue.)
Notes: 4